MEASUREMENTS

- During the time measurements, the CPU wasn’t busy with other “heavy” calculations, in order to measure the time more precisely
- The minimum time resolution is 1us and is implemented using the function clock_gettime() which is used before the start and after the end. Before measuring the end time, we have already compared the differences between original output and our output, in order to calculate the PSNR(Signal to Noise Ratio)
- The spreadsheet includes both -fast and -O0 measurements. However this report includes only the best of these 2
- All the measurements have an unique number in parenthesis. This number corresponds to the number of measurement in spreadsheet

LOOP INTERCHANGE

 Optimizations began from the source code 0_orig.c

Nested Loops:
 a) In line 109, we change the loop order, so the variable “i” runs in the outer loop and variable “j” in the inner. That leads in much better performance, improving. (Numbers 3, 5).

 b) Including the previous optimization, in line 46 we repeat the some methodology for the convolution2D function. That leads again to a 317 microsecond improve performance than Numbers( 4, 6)

However, if we try to do the same thing in the nested loop in line 127 the performance is getting worser per 12 microseconds than the previous one. ( Numbers 7,8)

COMMENTS:

-