MEASUREMENTS

- All measurements had the value of PSNR = inf
- During the time measurements, the CPU wasn’t busy with other “heavy” calculations, in order to measure the time more precisely
- The minimum time resolution is 1us and is implemented using the function clock_gettime() which is used before the start and after the end. Before measuring the end time, we have already compared the differences between original output and our output, in order to calculate the PSNR(Signal to Noise Ratio)
- The spreadsheet includes both -fast and -O0 measurements. However this report includes only the best of these 2
- All the measurements have an unique number in parenthesis. This number corresponds to the number of measurement in spreadsheet
- In (c) Code of Unroll optimization, I assumed that the defined size is 4096. If “#define SIZE 4096” changes, the loop must be rewritten
- In spreadsheet, with cyan color are the best variation per optimization technique for -O0 and with green are for -fast

- The optimization methods have been applied with the following order:
   Loop Interchange →

LOOP INTERCHANGE

- Optimizations began from the source code 0_orig.c

- We can apply that optimization, because we dont read from memory after the value has been modified by a previous loop iteration: e.g for ( i=0; i<N; i++)
        a[i] = a[i-1] + b[i];

- In line 109, we change the loop order, so the variable “i” runs in the outer loop and variable “j” in the inner. That leads in much better performance, 0.075837375secs with the -fast flag enabled
( Code (a) )

- Including the previous optimization, we repeat the some methodology for the convolution2D function. That leads again to a better impletentation,317 microseconds faster than the (a) ,using the -fast flag( Code (b) )

- However, if we try to do the same thing in the nested loop in line 127 the performance is getting worser per 12 microseconds than the previous one.
In the spreadsheet, number 7 uses the -O0 and number 8 the -fast( Code (c) )

- In the spreadsheet, code(a) corresponds to numbers number 3 and 5, code(b) to 4 and 6 and finally code(c) to 7 and 8

- So we keep the code(b) implementation and continue to the next optimization method.

LOOP UNROLLING

- Optimizations began from the source code 1_loopInter.c

- We start this optimization from the function convolution2D. This function contains the following nested loop:

- Firsty we try to unroll the inner loop. So the new code looks like the above( Code (a) )

- Now we measure with both -O0 and -fast and we find 2 complete different results. Flag -O0 seems not to decrease the execution time. Οn the contrary it increases it.
- On the other hand, -fast flags seems to create the best running time until now. So lets try to unroll the outer loop and make the nested loop fully unrolled ( Code (b) )

- While the automatic optimizations that compiler produces using the -fast decreases the latency, the -O0 flag seem to increase the execution’s time. Under that circumstances, compiler’s optimization like register allocation seem to do great job

- Now, we continue with further unrolling. Now look the nested loop in sobel function

- Try to unroll the inner loop. Assuming that SIZE=4096, the inner loop executes 4094 times. So we can unroll the loop N times, where 4094%N = 0. Possible values for N can be 2, or 8

- For N = 2, the execution time seems to be the same as the previous best time for both -fast and -O0. So no effect.

- If we try N =4, despite the fact that 4094%4 = 2, we get better time with PSNR=inf. The reason why choosing N = 4 isn’t illegal is because we don’t really count the last column and row of the array. So we keep N = 4. The following picture shows how the last executions for unroll factor = 4:

- If we try to unroll our loop 4 times instead of 2, the bellow code shows the unroll( Code (c) )

- We get an obvious decrease in total time using -fast, however for -O0 flag we again don’t take worthy results. Using the -fast, the total time has fallen to 0.0641150333 seconds.

- For N = 8, we get the same results as the previous one. So we stop at N=4

- Now, if we try to unroll the outer loop the code that we will be produced is going to increase a lot the size of the binary file. Also, after measurements for N = 2 or 4, the running time stays stable for -fast and gets even worser for -O0

- Now lets continue with the following loop:

- After measuring times, we don’t have any improvement. I tried unrolling these 2 loops and separately and together for N = 2, 4 and 8 but there was no improvement. Also tried to change loop order in order to increase locality for the inner loop, but it had no effect.

- In the spreadsheet, code(a) corresponds to numbers number 9 and 10, code(b) to 11 and 12 and finally code(c) to 13 and 14

- So we keep the code(c) implementation and continue to the next optimization method.

LOOP FUSION

- Optimizations began from the source code 2_loopUnrol.c

- In function sobel , we have the 2 following for nested for-loops:

   (a)

(b)

- If we notice these 2 nested loops, we can implement the Loop-Fusion technique with some changes in the 2nd loop. Firstly change loop order and then unroll partialy by j = j + 4. Lets take it step by step:

a) By changing loop order at (b) we have the same time as before, so:

b) Now we merge the two following loops ( code(a) )

- If we measure again the time is almost the double than before, 0.111 seconds and PSNR is 37.4392. We don’t continue more that optimization because we don’t improve our results

- Now lets go back at out 2_LoopUnrol.c code. If we try to merge the outer for-loops, the code looks like the following( code(b) )

- Now, if we run code(b) t using the -fast flag we have a small improvement in time, a bit less than 0.064 seconds. Unlike code(a), in code(b) the PSNR remains INF

- Also, if we run code(b) using the -O0 flag we have an important improvement in time. New best time for -O0 flag is 5.8283991 seconds

- Finally, I tried to merge the nested in into a (SIZE-1)*(SIZE-1) iterations but without success

- In the spreadsheet, code(a) corresponds to numbers number 15 and 16, code(b) to 17 and 18

- So we keep the code(b) implementation and continue to the next optimization method.

LOOP INLINING

- Optimizations began from the source code 3_loopFusion.c

- In function sobel , we call the function convolution2D two times. If we take out the optimizations with the loop unrolling and if we avoid calling the convolution2D function, the code looks like this: (code (a))

- If we count the time needed to execute, we have a new best time for -O0 flag, at 5.56secs but the -fast time is worser

- Now if we try to unroll the inner loop with factor=2, we don’t have either any improvement in -fast or -O0

- At this point, we create a branch in our code, because -fast uses different code from -O0 to run fast. So we are going to use 4_functInline.c for the -fast flag and 3_loopFusion.c for the -O0 flag

- In the spreadsheet, code(a) corresponds to numbers number 19 and 20

- So we keep the code(a) for -O0 implementation and continue to the next optimization method.

LOOP INLINING

- Optimizations began from the source code 3_loopFusion.c for the -fast flag and 4_funcInline.c for -O0 flag
4_funcInline.c

- Now start from the file that we had the fastest time for -O0 flag

- If we look the code (a) from Loop Inlining, we will find out that some values are reused. We are going to put these values out of this loop, so the code will look like the below code(code (a))

- Measuring with -O0 flag we get a better time. However -fast does not make improve any improve. - Now as you can see we have 3 accesses in memory per access. We can reduce it to 1 access and 2 moves. The following code shows that(code (b))

        (code (b))

- Now we get a much better time for -O0 flag. The time using -fast flag doesn’t improve its best performance.

- If we try something smarter like the picture below we dont take better results, so we don’t count that attempt

- So we keep code(b) as the fastest implementation of -O0 until now

3_loopFusion.c

- Now start from the file that we had the fastest time for -fast flag
- So, Lets recall that code:

- If we try to apply here Loop Invariant code optimization using the -fast, we don’t achieve better timing, so we keep that code without changing, hoping that next optimizations using -fast will improve the performance

- To summarize, the best time until now for -fast flag is 0.063534175 seconds(number 20 in spreadsheet and file: “3_loopFusion/3_loopFusion.c” ) and for -O0 flag is 5.4476366667 seconds(number 25 in spreadsheet and file: “5_loopInvariant/5_loopInvariant.c” )

- In the spreadsheet, code(b) corresponds to numbers number 25 and 26

- So we keep code(b) for the next optimization method
COMMON SUBEXPRESSION ELIMINATION

- Optimizations began from the source code 3_loopFusion.c for the -fast flag and 5_loopInvariant.c for -O0 flag

- Starting from file 3_loopFusion.c where we had the fastest time for -fast flag, we have the following code

- As we can see, some calculations are repeated at 3 times each. Let’s rewrite that code substituting the obsolete calculations with variable assignments

- However we don’t have any improvement in the timing neither in -fast or -O0 flag. So we don’t take that into account.
- I also tried to reduce the numbers of calls to convolution2D function by merging the into one call the vertical and horizontal calculation, however there wasn’t any improvement

- Now we continue with file 5_loopInvariant.c

- We start changing that code, so that we reduce memory accesses

- The idea is that in every iteration we shift a 3x3 array one position right, until the end of the line. So we dont’t have to access the memory for every single access, but we access only one new. Lets see the modified code. ( (code a1))

- Here we initialize our 3x3 tetragon for every new value of i and we shift the tetragon for every new value of j at the end of (i,j) iteration( (code a2))

- Now if we measure the timing, we achieve new best time, 5.3542seconds for -O0 flag. No improvements using the -fast flag

 In the spreadsheet, code(a) corresponds to numbers number 27 and 28

- So we keep code(a) and we continue to the next optimization

Strength Reduction